## Slide 1
Image manipulation using Fiji
Simon Lachambre
October 2018
http://unice.fr/plateformes/mica

## Slide 2
Program
What is a numerical image: Detectors for microscopy, Image dynamic, Image formats
What is ImageJ/Fiji : Download, Installation
First steps with Fiji : Menus description, Online documentation
Basic Operations : Histogram manipulation, Images transformations, Image calibrations, 3D visualization
Notes: Diapo à améliorer !! C’est nul !!!!

## Slide 3
What is a numerical image?

## Slide 4
A matrix of pixels
Each pixel is described by 3 values: - X and Y coordinate
- X and Y size (image resolution)
- Gray level, value (intensity) (Image Dynamic)
20 | 15 | 10 | 4 | 6 | 12 | 17 | 23 | 5 | 8
18 | 11 | 7 | 4 | 16 | 13 | 8 | 14 | 10 | 9
1 | 8 | 11 | 14 | 17 | 12 | 9 | 6 | 5 | 11
4 | 6 | 5 | 11 | 9 | 6 | 5 | 14 | 17 | 12
17 | 18 | 11 | 7 | 10 | 14 | 10 | 9 | 20 | 15
14 | 10 | 9 | 18 | 7 | 4 | 16 | 17 | 12 | 9
8 | 11 | 14 | 4 | 6 | 12 | 14 | 2 | 12 | 9
18 | 11 | 7 | 13 | 8 | 14 | 10 | 17 | 23 | 5
Definition
Example of fluorescence image

## Slide 5
e-
e-
e-
e-
e-
e-
e-
e-
e-
Analog-Digital
converter
20 | 15 | 10 | 4 | 6 | 12 | 17 | 23 | 5 | 8
18 | 11 | 7 | 4 | 16 | 13 | 8 | 14 | 10 | 9
1 | 8 | 11 | 14 | 17 | 12 | 9 | 6 | 5 | 11
4 | 6 | 5 | 11 | 9 | 6 | 5 | 14 | 17 | 12
17 | 18 | 11 | 7 | 10 | 14 | 10 | 9 | 20 | 15
14 | 10 | 9 | 18 | 7 | 4 | 16 | 17 | 12 | 9
8 | 11 | 14 | 4 | 6 | 12 | 14 | 2 | 12 | 9
18 | 11 | 7 | 13 | 8 | 14 | 10 | 17 | 23 | 5
photons
Potential well
CCD matrix
Amplifier
1 matrix divided in millions of wells  pixels = wide-field & spinning-disk
Each well collects the signal from a part of the observed field
CCD monochrome cameras
Notes: A charge-coupled device (CCD) is a device for the movement of electrical charge, usually from within the device to an area where the charge can be manipulated, for example conversion into a digital value. This is achieved by "shifting" the signals between stages within the device one at a time. CCDs move charge between capacitive bins in the device, with the shift allowing for the transfer of charge between bins.

## Slide 6
Example of a photomultiplier
Adapted to scanning techniques
Count the number of photons point by point  pixel per pixel then, convert in gray levels
Monochrome point detectors

## Slide 7
How to image a sample ?
Sample = continuous signal
Camera or PMT = light sensitive elements
Photons -> electrons
Image = discrete signal
Electrons -> Numerical value
Pixel = xy localisation + intensity of grey

## Slide 8
The image dynamic represents the number of gray levels to describe the sample signal on the numerical image.
A high dynamic range means a high precision in signal description
 Image treatment and analysis easier and more precise
Image dynamic
Eyes limit
Don’t trust your eyes in microscopy 
Notes: Dynamic of the cameras are limited by the intrinsic propertie of the well potentia depth. The number of electrons that can be stored in each well.
Some cameras are coding in 12 or 16 bits.
For point detectors in confocal, you decide the dynamic of your image and you set your parameters to fill this dynamic.

## Slide 9
Use all the possible dynamic of your image during your acquisitions !!
Histogram & Dynamic range
50 ms exposure time
300 ms exposure time

## Slide 10
What about color images?
Fluorescence acquisitions on monochrome detectors (monochromes CCDs or PMTs)
  The detectors count photons whatever their color : filters for selection
  Gray levels on the image are reflecting the number of photons
Coloration acquisitions on color cameras
  The sample is not emitting photons, but transmitted light is going through
  and some wavelengths are getting absorbed.
  The detectors sees real colors : Red, green, purple, brown (H&S/DAB…)
  Image coded in RGB: Every color can be defined by a composition of 3 primary colors
  A color image = 24 bits: R 8bits (0-255) G 8bits (0-255) B 8bits (0-255)

## Slide 11
Specificities of a color camera
Bayer filter (microlens with a RGB matrix: 1 B/1 R/ 2G )
> Mostly used
> Resolution loss
Rq : twice more green filters to get closer to human vision
Tri-CCDs (Dichroïc mirror to separate RGB)
Each color is collected on a different matrix, then recombined
> Keep maximal resolution
> Acquisition speed important
Notes: A three-CCD camera is a camera whose imaging system uses three separate charge-coupled devices (CCDs), each one taking a separate measurement of the primary colors, red, green, or blue light. Light coming into the lens is split by a trichroic prism assembly, which directs the appropriate wavelength ranges of light to their respective CCDs. The system is employed by still cameras, telecine systems, professional video cameras and some prosumer video cameras.
Compared to cameras with only one CCD, three-CCD cameras generally provide superior image quality through enhanced resolution and lower noise. By taking separate readings of red, green, and blue values for each pixel, three-CCD cameras achieve much better precision than single-CCD cameras. By contrast, almost all single-CCD cameras use a Bayer filter, which allows them to detect only one-third of the color information for each pixel. The other two-thirds must be interpolated with a demosaicing algorithm to 'fill in the gaps', resulting in a much lower effective resolution.[1]

## Slide 12
Tiff / Tif (Tagged Image File): No compression, data preserved, Metadata included (acquisition information). Heavy files. Preferred format
Jpeg / Jpg (Joint Photographic Experts Group): Compression resulting in information loss. Only used for presentations. No quantification possible
BMP (Bitmap) : No compression, very heavy, no back-up of the metadata.
GIF (Graphics Interchange Format) : Compression « without loss ». Creation of animations (web, presentations).
Vector image (SVG, DXF, DWG), … : format using segments, polygons and circles instead of pixels (matrix images). Resizable image with no quality loss. Demands high calculation power to get the highest observation quality.
Image formats
Notes: 3 Image Types: Lossy Compression and Metadata
Two critical aspects to keep in mind when converting images: Lossy compression Transcoding an image into a format that uses lossy compression will alter the original data, introducing artifacts (see 11: Warning on JPEG Compression↓). This is the case, e.g., for JPEG formats (with the exception of some JPEG2000 images that use lossless compression). As such, these types of data are intended for human interpretation only and are not suitable for quantitative analyses
Metadata In ImageJ, metadata associated with the image, such as scale, gray value calibration and user comments is only supported in tiff and zip (compressed tiff) images. In addition, selections and Overlays↓ are also saved in the TIFF header (cf. File▷Save [s]↓). None of the above is saved in other formats (cf. Native Formats↑).

## Slide 13
.lif = LASAF
.czi / .lsm = Zen Zeiss
.zvi = Axiovision Zeiss
.nd= MetaMorph (MDA)
.nd2 = NIS Nikon
Microscopy formats
Tiff / Tif = MetaMorph, MicroManager, export from NIS/ZEN/LASAF
Notes: 3 Image Types: Lossy Compression and Metadata
Two critical aspects to keep in mind when converting images: Lossy compression Transcoding an image into a format that uses lossy compression will alter the original data, introducing artifacts (see 11: Warning on JPEG Compression↓). This is the case, e.g., for JPEG formats (with the exception of some JPEG2000 images that use lossless compression). As such, these types of data are intended for human interpretation only and are not suitable for quantitative analyses
Metadata In ImageJ, metadata associated with the image, such as scale, gray value calibration and user comments is only supported in tiff and zip (compressed tiff) images. In addition, selections and Overlays↓ are also saved in the TIFF header (cf. File▷Save [s]↓). None of the above is saved in other formats (cf. Native Formats↑).

## Slide 14
Presentation of the software

## Slide 15
Website: http://rsbweb.nih.gov/ij/
First: ImageJ project
NIH project: Wayne Rasband
Open source
Collaborative and evolutive project: monthly version upgrades
Developers community: macros, plugins
Multi-platform compatibility: Windows, Mac OS, Linux, 32 and 64 bits
Notes: ImageJ can be downloaded from http://imagej.nih.gov/ij/download.html. Details on how to install ImageJ on Linux, Mac OS 9, Mac OS X and Windows [1] are available at http://imagej.nih.gov/ij/docs/install/ (Help▷Installation…↓ command). Specially useful are the platform-specific Troubleshooting and Known Problems sections. Fiji↓ installation is described at http://fiji.sc/wiki/index.php/Downloads.
The downloaded package may not contain the latest bug fixes so it is recommended to upgrade ImageJ right after a first installation. Updating IJ[?] consists only of running Help▷Update ImageJ…↓, which will install the latest ij.jar in the ImageJ folder (on Linux and Windows) or inside the ImageJ.app (on Mac OS X).
Help▷Update ImageJ…↓ can be used to upgrade (or downgrade) the ij.jar file to release updates or daily builds. Release updates are announced frequently on the IJ news website and are labelled alphabetically (e.g., v. 1.43m). Typically, these releases contain several new features and bug fixes, described in detail on the ImageJ News page. Daily builds, on the other hand, are labelled with numeric sub-indexes (e.g., v. 1.43n4) and are often released without documentation. Nevertheless, if available, release notes for daily builds can be found at http://imagej.nih.gov/ij/source/release-notes.html. When a release cycle ends (v. 1.42 ended with 1.42q, v. 1.43 with 1.43u, etc.) an installation package is created, downloadable from http://imagej.nih.gov/ij/download.html. Typically, this package is bundled with a small list of add-ons (Macros↓, Scripts↓ and Plugins↓).
Fiji comes as a portable application. That means that you do not have to install it; just download, unpack and start it.
First, go to Fiji's home page:
Now, select Extract All... from the File menu of the window which just popped up:
The extraction wizard will ask you for a destination on the second page; you should not use the default (which is a temporary directory), but select something like Desktop instead:
At the end, the extraction wizard will ask you if it should open the directory which contains the extracted files. Say yes, and open the extracted directory Fiji.app:
You can start Fiji by double-clicking on the fiji-win32 executable (on 64-bit systems, it is fiji-win64).
Next time you want to start Fiji, just open the Fiji.app directory on your desktop and double-click on the executable. To make things easier, you might want to create a shortcut to that executable and put it on the Desktop, into the Start menu, or into the QuickLaunch bar.
Caution: "Program Files" not recommended!
We strongly recommend that you store your Fiji.app directory somewhere in your user space (e.g., "C:\Users\[your name]\Fiji.app") rather than in "C:\Program Files" or other system-wide directory. If you move Fiji.app to such a directory, modern versions of Windows will deny Fiji write permission to its own directory structure, preventing it from being able to update.

## Slide 16
Virtual Java machine: translation of the source code
if(nbre==1)
{
selectWindow(proj_verte);
setTool("polygon");
waitForUser("Trace la région d'intérêt");
roiManager("Add");
run("Select None");
setThreshold(2700, 4095);
roiManager("select", 0);
run("Analyze Particles...", "size=1.80-Infinity circularity=0.00-1.00 show=Nothing add");
nRois=roiManager("count");
for(i=1; i<nRois; i++)
{
selectWindow(proj_rouge);
setThreshold(1950, 4095);
roiManager("select", i);
run("Set Measurements...", "area mean min display redirect=None decimal=3");
run("Analyze Particles...", "size=0-Infinity circularity=0.00-1.00 show=Nothing summarize");
}
selectWindow("Summary");
saveAs("Text", dir_out+proj_rouge+"roi.xls");
run("Close");
}
Source code
J for Java
Notes: ImageJ was designed with an open architecture that provides extensibility via Java plugins. Custom acquisition, analysis and processing plugins can be developed using ImageJ’s built in editor and Java compiler. User-written plugins make it possible to solve almost any image processing or analysis problem.
Being public domain open source software, an ImageJ user has the four essential freedoms defined by the Richard Stallman in 1986: 1) The freedom to run the program, for any purpose; 2) The freedom to study how the program works, and change it to make it do what you wish; 3) The freedom to redistribute copies so you can help your neighbor; 4) The freedom to improve the program, and release your improvements to the public, so that the whole community benefits.
ImageJ is being developed on Mac OS X using its built in editor and Java compiler, plus the BBEdit editor and the Ant build tool. The source code is freely available. The author, Wayne Rasband (wsr@nih.gov), is a Special Volunteer at the National Institute of Mental Health, Bethesda, Maryland, USA.

## Slide 17
Fiji Is Just ImageJ
Fiji comes as a portable application: No installation
Download, unpack and start
No administrator rights required
Package already containing a certain list of plugins
Automatic updates of ImageJ and installed plugins
Website: http://fiji.sc/Fiji

## Slide 18
Fiji interface
Toolset choice
Current toolset
Function tabs
Current action
Current version
ImageJ/Fiji community developing free tools
File: Open/Close, Save…
Edit: Copy/paste/cut, Selections parameters, Options…
Image: 2D/3D Image representation, Transformation, Stacks manipulation…
Process: Mathematical operations on images, Filtering…
Analyze: 2D/3D analysis tools
Plugins: Macros tools, Additional functions

## Slide 19
1
3
2
Online help
Notes: ImageJ alone is not that powerful: it’s real strength is the vast repertoire of Plugins↓ that extend ImageJ’s functionality beyond its basic core. The many hundreds, probably thousands, freely available plugins from contributors around the world play a pivotal role in ImageJ’s success [102]. Running Help▷Update ImageJ…↓, however, will not update any of the plugins you may have installed [B] .
ImageJ add-ons (Plugins↓, Scripts↓ and Macros↓) are available from several sources (ImageJ's plugins page [Help▷Plugins…↓], ImageJ Information and Documentation Portal and Fiji's webpage, among others) making manual updates of a daunting task. This reason alone, makes it extremely convenient the use of ImageJDistributions↑ bundled with a pre-organized collection of add-ons.
Below is a list of the most relevant projects that address the seeming difficult task of organizing and maintaining ImageJ beyond its basics. If you are a life scientist and have doubts about which distribution to choose you should opt for Fiji↓. It is heavily maintained, offers an automatic updater, improved scripting capabilities and ships with powerful plugins. More specialized adaptations of ImageJ are discussed in Software Packages Built on Top of ImageJ↓

## Slide 20
Basic operations

## Slide 21
One by one: File\Open
One or several images or a folder simultaneously: Drag & Drop on the Fiji window
Trick : Automatic reorganization of images: Window\Tile
Opening a ZEISS, LEICA, OLYMPUS or NIKON file: Bio-Formats plugin, LOCI
Virtual Stack: to open large image series that overcome the memory capacity
How to open images ?
Notes: Stacks
ImageJ can display multiple spatially or temporally related images in a single window. These image sets are called stacks. The images that make up a stack are called slices. In stacks, a pixel (which represents 2D image data in a bitmap image) becomes a voxel[?] (volumetric pixel), i.e., an intensity value on a regular grid in a three dimensional space.
All the slices in a stack must be the same size and bit depth. A scrollbar provides the ability to move through the slices and the slider is preceded by a play/pause icon that can be used to start/stop stack animation. Right-clicking on this icon runs the Animation Options… [Alt /]↓ dialog box.
Most ImageJ filters will, as an option, process all the slices in a stack. ImageJ opens multi-image TIFF files as a stack, and saves stacks as multi-image TIFFs. The File▷Import▷Raw…↓ command opens other multi-image, uncompressed files. A folder of images can be opened as a stack either by dragging and dropping the folder onto the ‘ImageJ’ window or or by choosing File▷Import▷Image Sequence…↓ To create a new stack, simply choose File▷New▷Image… [n]↓ and set the Slices field to a value greater than one. The Image▷Stacks▷↓ submenu contains commands for common stack operations.
Virtual stacks are disk resident (as opposed to RAM[?] resident) and are the only way to load image sequences that do not fit in RAM. There are several things to keep in mind when working with virtual stacks:
Virtual stacks are read-only, so changes made to the pixel data are not saved when you switch to a different slice. You can work around this by using macros (e.g., Process Virtual Stack) or the Process▷Batch▷Virtual Stack…↓ command
You can easily run out of memory using commands like Image▷Crop [X]↓ because any stack generated from commands that do not generate virtual stacks will be RAM resident.
TIFF virtual stacks can usually be accessed faster than JPEG virtual stacks. A JPEG sequence can be converted to TIFF by opening the JPEG images as a virtual stack and using File▷Save As▷Image Sequence…↓ to save in TIFF format
ImageJ appends a ‘(V)’ to the window title of virtual stacks and hyperstacks (see Hyperstacks↓). Several built-in ImageJ commands in the File▷Import▷↓ submenu have the ability to open virtual stacks, namely: TIFF Virtual Stack…↓, Image Sequence…↓, Raw…↓, Stack From List…↓, AVI…↓ (cf. Virtual Stack Opener). In addition, TIFF stacks can be open as virtual stacks by drag and drop (cf. 4: Opening Virtual Stacks by Drag & Drop↓).
LOCI Bio-Formats and RegisterVirtualStackSlices plugins, Process Virtual Stack and VirtualStackFromList macros
4 Opening Virtual Stacks by Drag & Drop
TIFF stacks with a .tif extension open as virtual stacks when dragged and dropped on the toolbar icon.

## Slide 22
Image information : at the top of the image
Title
Display Size (%)
Slices
Channels
Size (calibration and pixels)
Type 8 Vs. 16 bits
Weight

## Slide 23
Image information : in the metadata file
Path: Image \ Show info
Notes: Exercice: aller chercher des infos dans les metadata ex: tps expo, puissance laser

## Slide 24
Image information : in the metadata file
Path: Image \ Show info
Information about acquisition : exposure time, gain, duration, wavelenght, objective, …
Information about the image : title, size, resolution, location, …
Information about the display : range, magnification, threshold, region, …
Type of information depends on the file format, the acquisition software, and the microscopy type

## Slide 25
Path: Image \ Properties
Image information : calibration and scale bar
Wide-field: image pixel size =
Camera pixel size x binning
(Objective mag x intermediate mag)
Confocal: image pixel size decided by the user. Contained in the metadata file.
Path: Analyze \ Tools \ Scale Bar
From the general menu:

## Slide 26
Image
Histogram
Gray levels histogram
Path: Analyze \ Histogram
Gray levels
Number of pixels

## Slide 27
Image
Histogram
Gray levels histogram
Path: Analyze \ Histogram

## Slide 28
Path: Analyze \ Histogram
Gray levels histogram

## Slide 29
8 bits (2^8 = 256 gray levels)
16 bits (2^16 = 65536 gray levels)
Nb of pixels
GL
0
0
GL
Nb of pixels
255
65535
Image dynamic and Image type
0
GL
Nb of pixels
255
Nb of pixels
GL
0
65535
Good dynamic
Poor dynamic

## Slide 30
Conversion 16 -> 8 bits
 size : for poster or ppt presentation
Compatibility with some Fiji functions
Conversion 8 -> 16 bits
No interest !
Chart: 
| 0 | 255 | 510 | 765
 | 1000 | 2000 | 800 | 200
0 16384 32768 49152 65535
0 64 128 192 255
Nb of pixels
Gray levels
0 255 1024 2048 4095 … 65535
Gray levels
Nb of pixels
empty
Image dynamic and Image type
Notes: Ajouter une diapo sur les niveaux de gris 12 et 14 bits avec l’explication des octets

## Slide 31
0 255
Screen gray levels
Correlation between Image gray levels and Screen gray levels
Image gray levels
0 255
Linear modifications of the histogram
Path: Image \ Adjust \ B & C
Brightness & Contrast

## Slide 32
Brightness increasing
= Add a constant value to the correlation
Linear modifications of the histogram
Path: Image \ Adjust \ B & C
Brightness & Contrast
saturation
0 255
0 255
Screen gray levels
Image gray levels

## Slide 33
= Substract a constant value to the correlation
Linear modifications of the histogram
Path: Image \ Adjust \ B & C
Brightness & Contrast
Brightness decreasing
0 255
0 255
Screen gray levels
thresholding
Image gray levels

## Slide 34
Path: Image \ Adjust \ B & C
Linear modifications of the histogram
Brightness & Contrast
saturation
thresholding
Contrast increasing
= Increase of the slope of the correlation
Image gray levels
0 255
0 255
Screen gray levels

## Slide 35
Path: Image \ Adjust \ B & C
Linear modifications of the histogram
Brightness & Contrast
Contrast decreasing
= Decrease of the slope of the correlation
Gray levels
0 255
0 255

## Slide 36
Original image
Brightness decrease
Contrast increase
Contrast decrease
Brightness increase
Linear modifications of the histogram
Brightness & Contrast
Path: Image \ Adjust \ B & C

## Slide 37
Information loss
(gray levels deletion)
Changes applied definitively
Only on 8 bits images
Linear modifications of the histogram
Brightness & Contrast
Path: Image \ Adjust \ B & C

## Slide 38
Linear modifications of the histogram
Path: Image \ Adjust \ B & C
Brightness & Contrast
?
A
C
E
B
D
1
3
4
2
5
?
?
?

## Slide 39
Gamma function where p = pixel intensity
Enhances low gray levels and high gray levels of the image
Loss in the linear relationship between pixel’s gray values = Only useful for representation, no quantification possible
Non-linear modification of the histogram
Path: Process \ Math
Gamma

## Slide 40
Gamma decreasing
Increases of the low GL contrast, decreases of the high GL contrast
Non-linear modifications of the histogram
Gamma
Path: Process \ Math
Gamma < 1
File GL
0 255
Gray levels
Screen GL
Gray levels
0 255
0 255
0 255

## Slide 41
Gamma increasing
Decreases of the low GL contrast, increases of the high GL contrast
Non-linear modifications of the histogram
Gamma
Path: Process \ Math
Gamma > 1
File GL
0 255
Gray levels
Screen GL
Gray levels
0 255
0 255
0 255

## Slide 42
Image \ Adjust \ Size
Image \ Crop
Image \ Transform \ Flip
Image \ Transform \ Rotate
Image transformations

## Slide 43
Image saving
Save in tiff format to keep medata
Never modify raw files
Path: File \ Save As

## Slide 44
Stack Manipulations
Path: Image \ Stacks
Images Stack Hyperstack
Virtual Stack
Tools
Notes: Stack exo
Image sequence
Hyperstack (14z, 17t)

## Slide 45
Z project
Orthogonal view
3D Project
Projection on a 2D image of the pixels of an image stack based on intensity parameter (min, max, mean, etc …)
Simultaneous observation of the xy, xz and yz projections of an image stack
Rapid 3D reconstruction and rotation around a single axis, of an image stack
Path: Image \ Stacks \ …
3D visualization

## Slide 46
Raw image
Screen image
0 . 0 . 0
0 . 255 . 0
0
255
GL coding
RGB coding
Path: Image \ Look up Table
Look-up tables
Notes: LUT

## Slide 47
Application/creation of a look-up table
Overlay of the different fluorescence channels
Path: Image \ Color \ Merge channels
Path: Image \ Color \ Edit LUT
+
+
=
Look up tables / Merge channel
Path: Image \ Look up Table
Notes: Merge

## Slide 48
Creation of a stack of images
Convert to RGB
Path: Image \ Type \ RGB Color
Path: Image \ Stacks \ Images to Stack
Look up tables / Merge channel

## Slide 49
Images management
File > Import > Image Sequence… Open an image sequence with name criteria
Window > Tile Image reorganization on the desktop
Image selection > Entry Move the Fiji window to the foreground
File > Close All Close all opened images
File > Save As… Save with the chosen format
Process > Repeat Command (Ctrl + Maj + R) Repeat the last used command
Plugin > Utilities > Control Panel… Extraction of a specific menu on the desktop
Images manipulation
Image > Show Info… (Ctrl + I) Displays info about images
Analyze > Histogram (Ctrl + H) Displays the Gray level histogram
Image > Adjust > Brightness/Contrast… (Ctrl + Maj + C) Histogram linear modifications
Process > Math Apply mathematical operation to the selected image
Process > Subtract Background… Rolling ball radius to subtract the background
Process > Math > Gamma… Non linear modification of the histogram
Glossary

## Slide 50
Images manipulation
Process > Filters Apply filters to the selected image
Process > Filters > Convolve… Personalized filters
Process > FFT > FFT / Inverse FFT From spatial domain to frequency domain
Image > Type Image depth
Image > Crop (Ctrl + Maj + X) Crop following the selection
Image > Duplicate… Duplicate the image or the ROI on the image
Image > Adjust > Size… Modification of the image size
Edit > Invert (Ctrl + Maj + I) Invert all the gray levels of the image
Edit > Clear In the ROI, forces the pixels to a gray value of 0
Edit > Clear Outside Outside of the ROI, forces the pixels to a gray value of 0
Image > Hyperstack Manipulation of multi-dimensional images, 4-5D
Image > Transform Modification of images orientation
Images Calibration
Image > Properties… (Ctrl + P) Calibration of the pixel –voxel size
Glossary

## Slide 51
Management of colored channels
Image > Lookup Tables Apply false colors to the image
Image > Color > Edit LUT… Personalized LUTs
Image > Color > Split Channels Split colored channels from a stack or a composite
Image > Color > Merge Channels… Fusion of different colored channels
Figure assembly
Image > Stacks > Add slice Add an empty position to an image or an existing stack
Ctrl + C on Image1 & Ctrl + V on Image 2 Copy paste of an image to another one
Analyze > Tools > Scale bar… Add a scale bar to an image
3D visualization
Image > Stacks > Z Project… Stack projection on a 2D image
Image > Stacks > Orthogonal Views (Ctrl + Maj + H) Visualization XY/XZ/YZ
Image > Stacks > 3D Project… 3D reconstruction on one rotation axis
Plugins > 3D > ImageJ 3D Viewer 3D reconstruction
Glossary